## Slide 1
Marine-AI
A retrofittable AI advisory system for Philippine diesel passenger boats.*
Team SOLMATE · National AI Hackathon 2026 · Blue Economy / Clean Energy track
Public demo URL · public repo URL (both must resolve — required, or DQ)
Notes: One sentence. "We make boats already in the water burn less
fuel, break down less, and prove it — without replacing the boat or the engine."
SERVES (rubric): first impression; sets the retrofit framing that makes impact credible.

## Slide 2
The problem, in the operator's words
— ~5,000+ wooden/fiberglass diesel passenger boats in PH inter-island service.
— Fuel is the largest controllable operating cost; captains throttle on instinct.
— Breakdowns are discovered at sea, not scheduled at the dock.
— No emissions evidence → locked out of green financing and LGU/MARINA incentives.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
1/17
Notes: Three costs the operator already feels — fuel wasted, downtime
unplanned, and money left on the table for lack of a report they can't produce.
We did not invent a problem; we instrumented one.
SERVES (rubric): Impact & Feasibility (25%). Ground the pitch in a real operator, the captain from [`PRODUCT.md`](../PRODUCT.md).

## Slide 3
One system, three problems, one screen
— Three sensor systems → three parallel AI modules → one bridge display. 1. Speed Optimization — cheapest throttle that still meets the schedule. 2. Route Optimization — cheapest lawful track for the same arrival. 3. Predictive Maintenance — engine health, honest about its own maturity.
— Cross-cutting: Auditable Emissions Layer (Problem 3) rides on the fuel model.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
2/17
Notes: The architectural claim that ties it together: **there is one
fuel model in this system.** Speed, Route and Emissions are all scored by it, so
the litres a route saves and the litres a throttle saves can never come from two
different models. That is enforced by a test, not a promise.
SERVES (rubric): Innovation & Scalability; AI Strategy / Model Fit.

## Slide 4
What is real, and what is declared (HARDWARE DECLARATION)
— No retrofit hardware in this build. Declared, not hidden.
— Every telemetry frame carries source="simulator"; the contract has no default that could claim otherwise (packages/contracts/telemetry.py).
— The retrofit sensor kit is *specified* (RPM pickup, EGT probe, IMU, GPS, fuel- flow meter, weather feed) — the model inputs are exactly what that kit produces.
— The one real sensor path: the console can optionally read the browser's own GNSS and orientation, to place the vessel on the chart at your actual position. It feeds the map only. No engine, fuel or temperature stream is ever anything but simulated.
— The demo drives the real models with simulated telemetry, at real physics.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
3/17
Notes: This is the honesty slide, up front. We are a pre-sprint
software prototype. The sensors are named and the data they'd produce is exactly
what the models consume — so this is a working system waiting for a sensor kit,
not a mock-up. Saying so plainly is worth more than a staged hardware photo.
SERVES (rubric): Ethics/Data Integrity (this is the brief's declaration requirement); buys credibility for every later claim.

## Slide 5
Problem 1: Speed Optimization
— Product is not a recommended RPM. Product is the delta: litres/hour saved for the same arrival time.
— Physics decides how much power a speed costs in *these* conditions; the fuel model decides how many litres that power burns.
— Held-at-ETA optimiser: it never tells you to just go slower — it finds the cheapest throttle that still arrives on time.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
4/17
Notes: Demo beat — show head-sea vs calm at the same throttle; the
boat actually slows. In the old prototype the weather slider moved the readout
and never the boat; that bug is now a failing test if it ever returns.
SERVES (rubric): Technical Execution; the live-demo moment.

## Slide 6
The fuel model is a hybrid (AI STRATEGY / MODEL FIT)
— conditions + load → shaft power = physics (naval-architecture, calibratable).
— shaft power + wear → litres/hour = published diesel BSFC curve × XGBoost wear penalty.
— Why not end-to-end ML? No public dataset varies wind, current, wave or load — they are constants in it. A model "learning" them would ignore the inputs it acts on while reporting confidence on them.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
5/17
Notes: This is our single strongest data-integrity point and it maps
to the 20% "did you pick the right tool" criterion. We split the problem so the
part we can learn honestly is learned, and the part no dataset supports is
computed from physics with every coefficient named and per-vessel calibratable.
SERVES (rubric): AI Strategy / Data Integrity / Model Fit (20% semi-final). See [`docs/DEVIATIONS.md`](DEVIATIONS.md) §1.

## Slide 7
Model validation (TECHNICAL SOUNDNESS)
Model | Mean error, % of fuel burn
Assume every engine is healthy (a system with no fuel map) | 5.02%
Linear regression | 0.64%
XGBoost wear model | 0.09%
— Validated on whole held-out wear states (25% of decay pairs never seen in training) — not a random split, which would leak on a factorial grid.
— Honest weakness stated on-slide: load sampled at only 7 points; the wear axis is dense, the load axis is interpolated.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
6/17
Notes: The 5.02% row is the size of the problem. The gap from 0.64%
to 0.09% is why a tree earns its complexity over a straight line. Both baselines
print on every training run, so if the tree ever stops earning it, we'd see it.
SERVES (rubric): Technical Soundness (50% final, from the mentor report).

## Slide 8
Problem 2: Predictive Maintenance, honest about maturity
— Two phases, enforced in code, not just described:
  · Phase 1 (~first 24 months): "coolant temperature is drifting" — anomaly, never a component-level countdown.
  · Phase 2 (after labelled failure history exists): component-level RUL.
— The contract refuses to emit a Phase-2 prediction during Phase 1 (packages/contracts/maintenance.py). The honesty commitment is a validator.
— The Problem 1 → Problem 2 link is priced: a worn engine's fuel penalty is a line item in litres/hour and pesos/hour.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
7/17
Notes: Most predictive-maintenance demos overclaim on day one. Ours
physically cannot: the data model rejects a failure-date prediction before the
failure history that would justify it exists.
SERVES (rubric): Ethics/Bias (over-claim avoidance); Technical Soundness.
BUILD NOTE — resolve before pitching, do not read aloud:
**Build status note (delete before pitch):** the Phase-1 anomaly detector is
**built, tested and live on the display** — a pure-numpy ensemble of a robust
per-stream z-score and a PCA linear autoencoder, served by `POST /maintenance`
and rendered in the bridge Health zone. The demo beat to rehearse: open the
throttle and coolant *and* exhaust temperature both rise, and the panel stays
**nominal** (measured anomaly score 0.09) — because that correlation is what a
healthy engine does and the joint model learned it. Then inject a coolant creep
alone and it flags at 0.99, naming the coolant stream. A threshold detector
would have alarmed on the first and it is worth saying so out loud.

## Slide 9
Problem 3: The Auditable Emissions Layer
— Monthly CO₂-avoided report — exportable evidence for LGU / MARINA compliance and ESG-linked green financing. Zero extra sensors beyond Problems 1 & 2.
— CO₂ is not predicted — it is chemistry: 2.68 kg CO₂ per litre of marine diesel, from carbon mass balance, not a tuned constant.
— The claim that matters is the baseline: the vessel vs its *own* recorded burn on the *same* route before Marine-AI. Not a fleet average. A month that burned more reports as negative, not floored at zero.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
8/17
Notes: An "AI emissions model" that multiplied litres by a constant
and called it a prediction would be the least defensible thing we could build. So
we don't. The accuracy of the emissions report is inherited, transparently, from
the accuracy of the fuel model.
The line to land: **the report refuses to flatter you.** A voyage with no
baseline contributes its fuel and its CO2 to the totals but *not* to the avoided
figure, and the report names how many voyages that was. A month that burned more
than baseline reports as negative. Both of those make the headline number
smaller, and both are why the number is worth anything.
SERVES (rubric): Impact & Feasibility (the only deliverable aimed at the LGU / MARINA / green-finance stakeholder — a third of the problem statement).
BUILD NOTE — resolve before pitching, do not read aloud:
**Build status note (delete before pitch):** built and demonstrable as of
2026-07-26. `POST /voyages` records each crossing on arrival,
`GET /emissions/report.csv` is the export, and there is an "Export month" link
on the display. Live run: four crossings, the first three establish the route
history and honestly report **no baseline**, the fourth is measured against the
median of its own three priors — 2.841 L baseline vs 1.529 L actual,
**+3.52 kg CO2 avoided**, method `own_prior_route`. Demo it in that order; the
first three "no baseline" rows are the point, not a defect.

## Slide 10
Route Optimization: shared cost, real constraints
— Candidate tracks (direct great-circle + lateral offsets) → each leg costed through the same throttle optimiser as Speed. A one-leg route agrees with the throttle advisor to 1e-6 (enforced by test).
— Hard constraints: charted depth (a shorter track over a shoal is rejected, not costed) and forecast wave height.
— Honest baseline delta: savings = direct-route burn − planned-route burn, shown with its real sign.
— The forecast behind every leg is trained on 2.6 years of real Open-Meteo reanalysis data, not a hand-tuned field: gradient-boosted regression for wind/wave direction, a climatological lookup table for the rest — whichever won, per target, on six months of held-out weather. forecast_source says "gbm_climatology" on every response that used it.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
9/17
Notes: This is where "one fuel model" pays off. Route isn't a second,
disconnected product with its own cost assumptions — it reuses Speed's model
leg-by-leg, so a judge can't find two numbers that disagree. The forecast
question is the other one worth being ready for: "did you train the Temporal
Fusion Transformer?" The honest answer is better than a yes — a TFT forecasts
from recent observed history, and this endpoint has none to give it (no live
weather feed is wired into route planning, by design). What trains instead is
a position-and-time regression, and even that wasn't shipped as one
architecture: nine targets were raced against a climatological lookup table on
held-out real weather, and the table won on five of them. Both halves shipped.
SERVES (rubric): Innovation & Scalability; AI Strategy.
BUILD NOTE — resolve before pitching, do not read aloud:
**Build status note (delete before pitch):** the route engine, its constraints,
the `POST /route` API and the bridge Route zone that consumes it are built and
tested (276 tests green). The learned forecaster is **built** as of
2026-07-30 (`services/route/train.py`, `docs/DEVIATIONS.md` §13):
gradient-boosted regression for wind/wave direction plus a climatological
lookup table for wind/wave/current magnitude and current direction, trained
and validated against Open-Meteo's real historical archive. `forecast_source`
now reports `"gbm_climatology"`. **A caveat that got stronger, not weaker,
after training on real data:** swept across 16 (month, hour) combinations on
the Muelle-to-Jordan crossing, and separately on a longer 16 nm leg spanning
the full operating box, `savings_l` came back **zero every time** — 2026-07-30.
The trained climatology's spatial variation across a ~20 km box is genuinely
subtler than the analytic field's hand-tuned wind band, which was engineered
specifically to give the offset search something to find. This is the honest
cost of training on real data instead of a demo-shaped one: the model is more
believable and less demoable. Do not promise a nonzero savings figure on
Route without checking it live first. If the pitch needs one, either find a
real leg/time that produces one before the sprint, or present the zero
honestly — "the system checked and confirmed there is nothing to save on this
crossing today" is a legitimate answer for an advisory system to give, and
arguably a better one than a system that always finds a number.

## Slide 11
The interface: two seconds on a wet bridge
— Dark, high-contrast, oversized type — read at arm's length, in spray, at 05:40.
— Three zones by glance priority: Throttle (largest), Route, Health — all three live, each driven by its own endpoint (/advise, /route, /maintenance).
— Each zone ages independently and visibly: a route planned at the dock reads in minutes, the throttle advisory in seconds. One shared "last updated" would have made a stale throttle number look as trustworthy as a fresh one.
— Persistent trust bar: data freshness, connectivity, and `ADVISORY ONLY — CAPTAIN COMMANDS`.
— Filipino is first-class, not a translation afterthought.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
10/17
Notes: Every design decision falls out of one scene — a captain who
looks at the screen for under two seconds, twice a minute, one hand on the
throttle. Show the four POV modes / helm view here.
SERVES (rubric): Presentation (15%); Impact (usability by a non-engineer captain).

## Slide 12
The AI-authority boundary (ETHICS)
— The system never overrides the captain and never actuates the vessel. Every module advises; the captain decides.
— Safety cut-offs are rule-based and independent of every model (services/safety/rules.py, served at POST /safety). It imports no model, loads no artifact, and holds no state — a test asserts it can never import one. Same frame, same verdict, forever.
— Thresholds are readable off the page and checkable against an engine manual: coolant ≥105 °C, oil pressure ≤100 kPa, bus voltage outside 12.0–15.8 V, EGT ≥580 °C. A missing sensor is reported as skipped, never assumed safe.
— Language is never imperative: "1650 RPM saves 2.1 L/h", never "reduce to 1650".
— Claude writes the sentence; it never writes the number. The rewrite is compared against the optimiser's own sentence — same numbers exactly, no imperative clause — and thrown away if it differs. advisory_source on every frame names who wrote what the captain is reading.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
11/17
Notes: Under maritime liability the advisory boundary is a legal
requirement, not a stylistic choice. So we did not describe it, we built it: the
safety path is a separate module that consults nothing learned, and the test
suite fails if anyone ever imports a model into it. When you are asked "what
happens when your model is wrong" — this is the answer, and it is the one part
of the system that cannot be wrong in a new way.
Worth saying out loud: opening the throttle raises coolant and exhaust together
and the *health* model correctly stays nominal, while a coolant cutoff fires the
instant the threshold is crossed regardless of what any model thinks. Two
independent judgements, and the threshold always wins.
**The Claude line is the one to slow down on.** Every team at this event will
have an LLM in the stack. The question a technical judge asks is what stops it
from being wrong in public — and "we prompted it carefully" is not an answer.
Ours is: the model is handed a finished sentence and asked to say it better, and
the result is diffed against that sentence before it is displayed. Change a
number, and it is discarded. Open a clause with a command verb, and it is
discarded. The captain sees the deterministic sentence instead, and the panel
says so. That is the difference between an LLM in the product and an LLM in the
decision path, and we are only in the first one.
SERVES (rubric): Ethics/Bias (15% semi-final).
BUILD NOTE — resolve before pitching, do not read aloud:
**Build status note (delete before pitch):** the safety engine is **built,
wired and tested** (13 unit + 4 API tests) as of 2026-07-26. The Claude
advisory layer is **built, wired and tested** as of 2026-07-30
(`services/advisory/`, 28 tests) across the throttle, route and health
sentences. It requires `ANTHROPIC_API_KEY` on the deployed API — **without it
the demo is honest but shows `advisory_source: "template"` throughout**, so
set the key in the Vercel project before recording the screencast, and check
`GET /health` reports `"advisory_layer": "claude"`.

## Slide 13
Data & models, cited (DATA INTEGRITY — REQUIRED CITATIONS)
Source | Role | Licence
UCI *CBM of Naval Propulsion Plants* (gas turbine) | Wear-penalty model, as a documented proxy | Open (UCI ML)
NASA C-MAPSS | Evaluated for maintenance pretraining; not used — the detector learns each vessel's own baseline | US Gov public domain
Published marine-diesel BSFC part-load data | Healthy-burn curve | Literature
Open-Meteo Marine | Wind / wave / current forecast | CC BY 4.0
GEBCO bathymetry | Depth constraint *(intended; not yet integrated)* | Open
Sentinel-2 cloudless (EOX) | Satellite basemap / helm horizon | CC BY 4.0
Natural Earth | Coastline vector | Public domain
— Every dataset is public or licensed; no scraped or unlicensed imagery. Google/Bing/Esri tiles were considered and rejected on their terms.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
12/17
Notes: The brief grades "use only licensed or public datasets" and
requires external models cited in the deck — this slide is that requirement,
discharged. Note the three honest caveats we lead with: the anchor dataset is a
gas turbine used only for the *dimensionless* wear penalty; GEBCO is intended but
not yet wired; and C-MAPSS is cited because we evaluated it, not because it
trains anything — the Phase 1 detector learns each vessel's own normal instead,
which is the better fit anyway, since a turbofan's degradation modes are not a
marine diesel's.
SERVES (rubric): Data Integrity (20% semi-final); the brief's citation requirement.

## Slide 14
We list our own deviations
— We keep a DEVIATIONS.md — every place the build departs from our submitted profile, why, and what it costs. Highlights:
  · Fuel model is hybrid, not end-to-end XGBoost.
  · Anchor dataset is a gas turbine proxy; only the wear penalty transfers — borrowing its part-load curve would have overstated savings ~5× in our favour.
  · FEMTO dropped: it's 25.6 kHz bench data; the spec'd IMU logs at ~1 Hz.
  · Stack: ONNX (not TFLite) — 85 MB vs 358 MB runtime; Supabase (not Timescale); Open-Meteo (PAGASA has no public API).
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
13/17
Notes: A judge will find these by reading the source. Finding them
here, with the reasoning attached, is a completely different experience from
discovering the paper overstated something. This slide is a trust asset.
SERVES (rubric): Technical Soundness; Ethics/Data Integrity; Q&A defence.

## Slide 15
Impact & feasibility
— Retrofit, not replacement — installs on boats already in service; the whole addressable fleet is reachable without new hulls.
— Measured outcomes: litres/nm down, pesos/voyage down, unscheduled downtime converted to scheduled dry-docking, CO₂-avoided evidence produced monthly.
— Three stakeholders, three surfaces: captain (bridge screen), owner/cooperative (savings + emissions report), LGU/MARINA/ESG lenders (exported evidence).
— Runs as a serverless function (85 MB serving image) — cheap to operate, same argument for an on-vessel edge unit.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
14/17
Notes: Feasibility is the retrofit story plus the cost story. We're
not asking an operator to buy a boat; we're asking them to bolt on a sensor kit
that pays for itself in fuel.
SERVES (rubric): Impact & Feasibility (25%); Scalability (10%).

## Slide 16
Scalability & roadmap
— Per-vessel calibration: the physics coefficients fit to each boat's own fuel-flow meter (calibrate_admiralty) — the model becomes a model of *that* boat.
— Fleet path: same schema scales from one boat to a cooperative's fleet; SQL is portable to TimescaleDB when volume justifies it.
— Near-term: wire GEBCO depth; train the route forecaster on the Open-Meteo archive; fit per-vessel health baselines from logged telemetry in place of the demo default; PAGASA integration via data-sharing.
— Longer-term: AIS traffic avoidance (reserved in the contract today).
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
15/17
Notes: Everything on the roadmap is a *named seam in the code today*,
not a wish. The forecaster loads through one function; AIS has a reserved contract
field; depth has a provider protocol. Scaling is wiring, not rewriting.
SERVES (rubric): Innovation & Scalability (10%).

## Slide 17
Team & close
— Team SOLMATE — roles.
— One line: *"Marine-AI: less fuel, fewer breakdowns, and the receipts to prove it — on the boats that are already out there."*
— Public demo URL · repo URL · this deck.
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
16/17
Notes: Close on the retrofit promise and the honesty posture. Invite
the Q&A — the deviations slide means we welcome the hard questions.
---

## Slide 18
Appendix / backup slides (for Q&A, not in the main flow)
— A1 — Fuel model math: the BSFC bathtub curve, the derived (not chosen) enrichment coefficient, the idle-burn floor.
— A2 — Why ONNX earned its keep: 358 MB → 85 MB; export gated at 1e-4 drift (observed 1.5e-6).
— A3 — Route costing detail: candidate sweep, per-leg optimiser reuse, the 1e-6 agreement test.
— A4 — The wear→fuel bridge: EGT-excess-over-baseline as the wear signal (r=0.99 in training), ratio-against-healthy to cancel boundary bias.
— A5 — Full deviations table (12 deliberate departures from DEVIATIONS.md, plus the "Still outstanding" table of what is not built yet). Bring both. The second one is the harder slide and the more convincing one.
— A6 — The safety path: the rule table, the thresholds, and the test that fails if a model is ever imported into it.
— ---
Marine-AI · Team SOLMATE · ADVISORY ONLY — CAPTAIN COMMANDS
17/17